| Program :- B.Tech | Faculty Name :- Roshan Datt Kashyap | Sem. :- 6Th |
| --- | --- | --- |
| Course Name :- HMT | Course Code :- C037613(037) | Max Marks :- 20 |

Assignment- 1

Note: - Each Question carries 4 marks.

1.  Derive general equation of heat conduction in cylindrical coordinates for 3 dimensions. 							 		            	  	    (CO - 1, PO - 2, Level - 3) [4]

2. The temperature on the two surfaces of a 40 mm thick steel plate (K = 32 W/m°C) having a uniform volumetric heat generation of 25 x 106 W/m³ are 210°C and 150°C. Neglecting the end effects. Determine the following:

(i) The temperature distribution across the plane

(ii)The value and position of the maximum temperature (completely derive the equation for position and value )

(iii) The flow of heat from each surface of the Plate.			    (CO - 2, PO - 3, Level - 1) [4]

3. A stainless steel wire (conductivity = 27 w/m-deg and resistivity = 65 μ ohm-cm) of length 2.5 m in and diameter 3.5 mm is submerged in a fluid at 45°C and an electric current of intensity 320 amps passes through it. If conductance at the wire surface is 3.8 kW/m²-deg, workout the steady state temperature at the centre and at the surface of the wire.          				    (CO - 3, PO - 1, Level - 1) [4]

4. A steel ball of 5 cm diameter at 500°C is suddenly placed in a controlled environment at 100°C. Taking the following data, find the time required for the ball to attain a temperature of 150°C.

Cp = 450 J/kg-°C, h = 10 W/m²-K, K= 35 w/ m-K, Density = 800 kg/m³.	     (CO - 2, PO - 3, Level -1) [4]

5. Derive an expression for temperature distribution, heat transfer for an infinitely long pin fin.											   (CO - 2, PO - 3,  Level - 3) [4]

| Program: - B Tech MECHANICAL | Faculty Name:- Dr. P S RAO | Sem:- 6th |
| --- | --- | --- |
| Course Name:-POWER PLANT ENGINEERING | Course Code: - C037632(037) | Max Marks:- 20 |

Assignment- 1

Note: - Each Question carries 4 marks.

- How many types of power stations used in India? Explain in brief?								                                                     (CO-1, PO-1, Level-2) [4]

- Discuss elements of electric power system and explain primary and secondary power distribution system.				                    (CO-2, PO-1&2, 2, Level-1) [4]

- Draw a neat layout of hydroelectric power plant and nuclear power plant.							(CO-1&2, PO-2, 2, Level-2&3) [4]

- Discuss the importance of following elements of steam power plant:

Ash handling system, air preheater, steam reheater, feed water preheater and deaerator.								           (CO-1, PO-1, 2, Level-1)   [4]

- Briefly explain feed water treatment?                         	(CO-3, PO-2,Level-2)       [4]

| Program: -B.TECH. | Faculty Name:- ROBIN BABU | Sem:-6TH |
| --- | --- | --- |
| Course Name:- DESIGN OF MACHINE ELEMENT | Course Code: -C037611(037) | Max Marks:- 20 |

Assignment- 1

Note: - Each Question carries 4 marks.

1.Write short notes on Maximum Shear Stress theory. Explain in brief.

2. Explain Notch sensitivity in brief.

3.Write short notes on Endurance limit. Draw and Explain S-N curve for steel.

4.A plain stresselement hasσx = 80 MPa, σy = 0 MPa and τxy = 50MPa. Find the principal stresses and directions using Mohr’s circle.

5.The 2-mm-thick bar shown in Fig. is loaded axially with a constant force of10 kN. The bar material has been heat treated and quenched to raise its strength, butas a consequence it has lost most of its ductility. It is desired to drill a hole throughthe center of the 40-mm face of the plate to allow a cable to pass through it. A 4-mmhole is sufficient for the cable to fit, but an 8-mm drill is readily available. Will acrack be more likely to initiate at the larger hole, the smaller hole, or at the fillet?

| Program: -B.Tech. | Faculty Name:- CHANDRA SHEKHAR | Sem:-6TH |
| --- | --- | --- |
| Course Name:- Manufacturing Technology | Course Code: -C037612(037) | Max Marks:- 20 |

Assignment- 1

Note: - Each Question carries 4 marks.

1.Explain external cylindrical grinding and surface grinding with neat sketch.											[4]

2.Write down special features of grinding.					[4]

3.What are the characteristics of grinding wheels ?		[4]

4.Explain briefly with respect to following parameters for Electrical Discharge Machining:								[4]

(i) Principle

(ii) Advantages

(iii) Limitations

(iv) Process parameters

(v) Surface finish

5.Explain ‘Electro Chemical Machining’ (ECM) and give its applications.										[4]

| Program: BTech | Faculty Name: Mr. Pravin Chandrakar | Sem.: VI |
| --- | --- | --- |
| Course Name: Principles of Management | Course Code: C000635(037) | Max Marks: 20 |

Assignment- 1

| QN | Question | CO | PO | Level | Marks |
| --- | --- | --- | --- | --- | --- |
| 1 | What are the basic functions of management? Describe in brief. | 1 | 1 | 1 | 4 |
| 2 | Explain the social responsibilities of manager. | 1 | 8 | 2 | 4 |
| 3 | Write down a short note on Materials Requirement Planning. | 1 | 2 | 2 | 4 |
| 4 | What are the merits and limitations of Advertising? | 2 | 2 | 4 | 4 |
| 5 | Describe the ABC Analysis in Inventory Management. | 2 | 2 | 4 | 4 |