| Program: - B.Tech | Faculty Name:- RICHA SAHU | Sem:- 7 |
| --- | --- | --- |
| Course Name:- PAS | Course Code: - D024712(024) | Max Marks:-20 |

Assignment- 1

Even Session (July-Dec 2022)

Note: - Each Question carries 4 marks.

1..A transmission line conductor crossing a river is supported from two towers at height 30 m and 80 m above the water level. The horizontal distance between the towers is 450 m. If the tension in the conductor is 1500 kg and weight of the conductor is 1.4 kg/m length, find the minimum clearance of conductor and water and clearance mid way between the supports.						                                                       (CO-1, PO-2,  Level-3)   	[4]

2	Explain in details:-

(i) Suspension insulator

(ii) Any one method of improving string efficiency.   	       (CO-1, PO-,2 Level- 2)   	[4]

3.  Explain radial and ring main system in details.	                   (CO-2, PO- 2, Level-2)   	[4]

4..What are the general consideration govern for designing the distribution system .Explain their importance .	                                                                               (CO-2, PO-2 , Level-3)   	[4]

5.Explain suppression coil grounding in detail with 	diagram. 						                                                                                            (CO-3  PO- 2 Level-2)   	[4]

| Program: - ELECTRICAL | Faculty Name:- PRASHANT BAWANEY | Sem:- 7TH |
| --- | --- | --- |
| Course Name:- ENERGY AUDITING & MANAGEMENT | Course Code: - D024731(024) | Max Marks:-20 |

Assignment- I

Note: - Each Question carry 4 marks.

1.	What is meaning of Primary and Secondary Energy.		(CO-1, PO-2, Level-2)   	[4]

2.	What is Energy Conservation.					(CO-1, PO-1, Level-1)   	[4]

3.	Write about different type of energy audit			(CO-2, PO-2, Level-2)   	[4]

4.	Explain the energy costing.		        			(CO-2, PO-2, Level-2)   	[4]

5.	Give the constructional details of Energy efficient Motors. 	(CO-3, PO-1, Level-1)   	[4]

| Program: -B.Tech | Faculty Name:- Akash Dewangan | Sem:-7th |
| --- | --- | --- |
| Course Name:- Electric Drives | Course Code: - D024711(024) | Max Marks:-20 |

Assignment- I

Note: - Each Question carry 4 marks.

1. Describe four quadrant operation of a drive with suitable example. (CO-1, PO-1, Level-2) 	[4]

2. Derive expression for moment of inertia of a flywheel connected to shaft of a drive.

(CO-2, PO-2, Level-3)   	[4]

3. Describe the working principal of multi motor drive with progressive change in reference signal. Draw neat diagrams.					                          (CO-2, PO-1, Level-2)             	[4]

4. What are advantages of close loop control of drive? Explain current limit control scheme with neat diagram.							(CO-2, PO-4, Level-2)   	[4]

5. Describe the working principal of single phase fully controlled d.c. separately exited motor. Draw neat diagram and write necessary equations.		 		(CO-3, PO-1, Level-3)   	[4]

| Program: -B.Tech | Faculty Name:-Ashish Dewangan | Sem:-7th |
| --- | --- | --- |
| Course Name:- High Voltage Engg | Course Code: - D024713(024) | Max Marks:-20 |

Assignment- I

Note: - Each Question carry 4 marks.

1. Explain different types of ionization in detail.                           (CO-1, PO-1, Level-2)  	 	[4]

2. Explain uniform and non uniform filed.	                           (CO-1, PO-2, Level-3)   	[4]

3. Write short note on cavitation and bubble theory.                      (CO-2, PO-1, Level-2)             	[4]

4. Explain breakdown due to treeing and tracking.		(CO-2, PO-4, Level-2)   	[4]

5. Write short note on Electro static Generators. 		(CO-3, PO-1, Level-3)   	[4]

| Program: -B. Tech | Faculty Name:- NF | Sem:-7th |
| --- | --- | --- |
| Course Name:- Non Conventional Energy Source | Course Code: - D000724(025) | Max Marks:-20 |

Assignment- I

Note: - Each Question carry 4 marks.

1. Write the merits and demerits of non-conventional energy sources with conventional.					                           				(CO-1, PO-1, Level-2)  	 	[4]

2. Write short notes on:

(i) Agriculture and industrial process heat	(ii) Solar pumping.										                           (CO-2, PO-3, Level-3)   	[4]

3. What do you mean by greenhouse enumerate the main types of greenhouses										.                         (CO-2, PO-1, Level-2)             	[4]

4. Write the criteria for the selection for wind energy convention system?												(CO-3, PO-4, Level-2)   	[4]

5. Write short notes on Horizontal Axis and Vertical Axis wind turbine generation units.									 		(CO-3, PO-1, Level-3)   	[4]