| Program: -B. Tech | Faculty Name:- Dr. SHAILENDRA VERMA | Sem:-IV |
| --- | --- | --- |
| Course Name:- Electrical Machines – II | Course Code: - B024413(024) | Max Marks:-20 |

Assignment- I

Note: - Each Question carry 4 marks.

Q.1.. A 12 – Pole, 3 – phase, 600 –V, 50 – Hz, star – connected motor has rotor – resistance and standstill reactance of 0.03 and 0.05 ohm per phase respectively. Calculate :(a) speed of maximum torque. (b) ratio of full –load torque to maximum torque, if the full – load speed is 495 rpm.                                                                                             (CO-2, PO-2, Level-2)	       [4]

Q.2. A 746 – kW, 3- phase, 50 – Hz, 16 – pole induction motor has a rotor impedance of (0.02 + j 0.15) W at standstill. Full – load torque is obtained at 360 rpm. Calculate (i) the ratio of maximum to full – load torque (ii) the speed of maximum torque and (iii) the rotor resistance to be added to get maximum starting torque.                                         (CO-2, PO-2, Level-3)	        [4]

Q.3 The power input to a 500 V, 50 – Hz, 6 – pole, 3 – phase induction motor running at 975 rpm is 40 kW. The stator losses are 1 kW and the friction and windage losses total 2 kW. Calculate : (i) the slip (ii) the rotor copper loss (iii) shaft power and (iv) the efficiency.

(CO-2, PO-2, Level-2)	 [4]

Q.4. Derive formula for Kp and Kd ?                                                                         (CO-1, PO-2, Level-3)       [4]

Q.5. What are different Methods of starting of three phase induction motor ?

(CO-2, PO-2, Level-3)     [4]

| Program: -B. Tech | Faculty Name:-Ashish Dewangan | Sem:-4th |
| --- | --- | --- |
| Course Name:- AE | Course Code: - B024415 (024) | Max Marks:-20 |

Assignment- I

Note: - Each Question carry 4 marks.

1.Write short note on BJT

(CO-1, PO-1, Level-2)   	[4]

2. Explain biasing and its different types.

(CO-1, PO-2, Level-3)   	[4]

3. Explain depletion type MOSFET in detail	                          (CO-2, PO-1, Level-2)   							                                                                    	                           [4]

4. Explain   common drain amplifier in detail	                           (CO-2, PO-4, Level-4)   	[4]

5. What is the difference between BJT and FET                                    (CO-3, PO-1, Level-1)   	[4]

| Program: - B. Tech | Faculty Name:- RICHA SAHU | Sem:- 4TH |
| --- | --- | --- |
| Course Name:- EMF | Course Code: - B024411(024) | Max Marks:-20 |

Assignment- 1

Even Session (April-May 2023)

Note: - Each Question carries 4 marks.

- Derive an expression for electric field intensity at any point due to a line charge with uniform charge density on the infinitely long z-axis.

(CO-1 PO-1  Level-2)   [4]

- An infinitely long, uniformly line charge is located at y=3, z=5. If pL=30 nC/m,

Find E at :

- The origin

- PB(0,6,1)

(CO-1, PO-2, Level-2 )   [4]

- State and prove divergence theorem.                   (CO-2 PO-2 , Level-2)   	[4]

- Derive the expression for potential difference in the field of a point charge.

(CO-2, PO-2 , Level-3)   	[4]

- A point charge Q lies at the origin. Show that ▼. D=0 everywhere except origin.

(CO-2, PO-2 , Level-3)   	[4]

| Program: -B. Tech. | Faculty Name:-Akash Dewangan | Sem:-4th |
| --- | --- | --- |
| Course Name: Signals and Systems | Course Code: - B024414(024) | Max Marks:-20 |

Assignment- I

Note: - Each question carry 4 marks.

1. Give definition, mathematical expression and graphical representation for following elementary signals:

- Unit impulse

- Unit step

- Unit ramp

- Sinusoidal

- Rectangular pulse

- Exponential signal						     (CO-1, PO-1, Level-3)  [4]

2. Compare energy and power signal.			          	     (CO-1, PO-1, Level-2)  [4]

3. Explain the following signals with help of illustrations:

- One-Dimension & Multi-Dimension

- Continuous-time & Discrete-time

- Continuous-valued & Discrete-valued

- Even and Odd continuous time signals			    (CO-1, PO-1, Level-3)   [4]

4. Describe the input-output behavior with periodic convergent inputs.

(CO-2, PO-2, Level-2)  [4]

5. Define the concept of convolution and explain its significance in signal processing.			 	 	    						    (CO-2, PO-2, Level-2)   [4]

| Program: - B.Tech (Electrical Engg.) | Faculty Name:- Prashant Bawaney | Sem:- 4th |
| --- | --- | --- |
| Course Name:- Power Systems – I | Course Code: -B024412(024) | Max Marks:- 20 |

Assignment- 1

Note: - Each Question carries 4 marks.

- Give the method of calculating the inductance of a bundled conductor line.

[Co-2, Po-1, Level-1]	 [4]

- What is the effect of earth on line capacitance?

[Co-2, Po-2, Level-1]      [4]

- What is the purpose of an overhead transmission line? How are these line classified?

[Co-3, Po-1, Level-1]      [4]

- What do you understand by generalized circuit constants of a transmission line?

[Co-3, Po-1, Level-2]      [4]

- Compare the merits and demerits of underground system versus overhead system.

[Co-4, Po-3, Level-1]       [4]